## Slide 1
A Multi-Domain Foundation Model for Prognostics & Health Management
Pre-trained across 4 PHM datasets · Evaluated on classification & RUL tasks
Zaynab Raounak

## Slide 2
Why a Foundation Model for PHM?
Problem
PHM models are typically trained from scratch per dataset — limited by small, domain-specific data.
Idea
Pre-train a single transformer backbone across multiple PHM domains, then fine-tune per task.
Goal
Leverage cross-domain patterns (vibration signatures, degradation trends) to improve accuracy and data efficiency.

## Slide 3
Training Datasets
CWRU
Bearing Fault Diagnosis
1 ch · 12 kHz
Classification (4 classes)
PRONOSTIA
Bearing Degradation
2 ch · 25.6 kHz
RUL Regression
CMAPSS
Turbofan Engine
14 ch · cycle-based
Classification + RUL
MFPT
Bearing Fault Diagnosis
1 ch · 97.6 kHz
Classification (3 classes)

## Slide 4
Model Architecture
Input Signals
Multi-channel time series
▶
Patch Embedding
64-sample patches linear projection
▶
Transformer Encoder
4 layers, 8 heads d_model = 128
▶
Domain Embedding
Frequency + Dataset ID
▶
Projector MLP
Shared latent representation
▶
Task Heads
Per-dataset cls / rul heads
Key: Channel-independent processing | Balanced domain sampling | Multi-task loss (CE + MSE)

## Slide 5
Classification Results
Average Classification Accuracy
98.12%
+2.6% over baseline
Dataset
Baseline
Foundation
Gain
CWRU
92.75%
97.95%
+5.20%
MFPT
98.29%
98.29%
0.00%
CMAPSS
—
—
—
F1 Score (Macro)
CWRU: 93.96% → 98.27% (+4.31%)
MFPT: 97.53% → 97.53% ( 0.00%)
Key Takeaway
The foundation model achieves near-perfect classification on CWRU (+5.2% over CNN baseline) while maintaining parity on MFPT. Cross-domain pretraining provides the biggest lift on CWRU, where the model benefits from vibration patterns learned across all four datasets.

## Slide 6
Cross-Domain Generalization (Leave-One-Out)
Model pre-trained on 3 datasets, then fine-tuned and tested on the held-out dataset
CWRU held out
Accuracy
96.38%
F1 Score
96.91%
Trained on: PRONOSTIA + CMAPSS + MFPT
MFPT held out
Accuracy
97.44%
F1 Score
96.34%
Trained on: CWRU + PRONOSTIA + CMAPSS
The model generalises to unseen domains with minimal accuracy loss — demonstrating that the shared transformer backbone captures transferable vibration features across different machinery types.

## Slide 7
Low-Data Regime Analysis
Baseline CNN accuracy with reduced training data (CWRU)
10% data
42.4%
20% data
41.4%
50% data
48.3%
100% data
48.6%
Even at 10% training data, the baseline achieves 42.4% — a foundation model pre-trained on related domains can significantly boost this via transfer learning, reducing the labelled data requirement.

## Slide 8
Summary & Next Steps
Achievements
✓ 98.12% avg classification accuracy (+2.6% over baseline)
✓ CWRU accuracy: 97.95% (+5.2% gain from pre-training)
✓ Strong cross-domain transfer (96-97% on held-out domains)
✓ Unified architecture handles 4 PHM domains
✓ Channel-independent design supports 1 to 14 channels
Next Steps
→ Improve RUL regression with refined head architecture
→ Add more PHM domains (Paderborn, IMS, etc.)
→ Evaluate few-shot transfer with foundation features
→ Explore self-supervised pre-training objectives
→ Benchmark against state-of-the-art per-dataset models
A single pre-trained backbone outperforms per-dataset CNNs on classification — demonstrating the viability of foundation models for PHM.